Migrate a RTAI Application to RT-Preempt
-
A case study
linu
tronix

---
Initial position
Linux-2.4.26 + RTAI
Existing Application (Automated Test Equipment)
  - Audio stimulation
  - Frequency generator (1 - 1000Hz)
  - Power fail scenarios
  - Serial data stream capture and analysis

---
Goal
Linux-2.6 + Realtime Extension
Make the application code more modular and portable. Code must be usable on an unmodified kernel
  - Application Programming Interface: POSIX

---
Which real-time extension to use ?
Available choices:
RT-Linux
  - Excluded due to licensing
RTAI/Xenomai
RT-Preempt

---
Xenomai vs. RT-Preempt
Xenomai:
Dual Kernel approach
Separate libraries
RTAI migration skin allows easy transition of the existing code
RT-Preempt
Single Kernel
Standard glibc (+ patches)
Reimplementation of the code necessary

---
Xenomai first choice ?
POSIX interface not fully implemented
One to one usage of existing code did not work out
Adds 300k+ binary code size and 250k+ data size to the kernel
Code has to be modified / recompiled to use on vanilla Linux
Unclear project situation after the RTAI split

---
What about RT-Preempt ?
POSIX interface fully implemented
Small increase in kernel size (36k code, 15k data)
Strong and mainline visible development
Code runs unmodified on vanilla Linux
Performance evaluation positive

---
How to migrate smoothly and fast ?
Stub device drivers implemented first, so application and device driver development can go in parallel
Userspace:
Complete redesign of the application
Reuse of code evaluated
Modular functionalities implemented in parallel
Kernel:
Usage of a framework for industrial I/Os
Driver implementation restricted to absolute necessary low level functions

---
What's the result ?
Two weeks of implementation time. (4 engineers)
Functional prototype
Shiny new modular design
Impressive decrease of code lines:
Original RTAI code:	12200
New implementation: 7300

---
Performance results
Environment:
  - Pentium M 1,4GHz
  - Custom made interface hardware (Audio stimulation, Frequency stimulation, Fieldbus interface)

---
Performance results
Audio: Interrupt driven refill of the D/A buffer (Period: 720us)
Maximum Latency
(Hardware interrupt -> Last FIFO entry written): 220us
ISR (Low level ACK)
Wakeup UT
Hardware
Buffer Refill Task
Fill FIFO with pre calculated values
Calculate next buffer or read from mmapped file
mmap

---
Performance results
Frequency stimulation: 1-8 Timers toggle an output pin
Frequency jitter: max. 60µs
Hardware
High Resolution timers
Timer callback
Driver
Frequency Control Task
Command pattern processing

---
Performance results
Data stream capture from the device under test
ISR (Low level ACK)
Wakeup UT
Hardware
Buffer Readout Task
Read FIFO
Store values into a Ring Buffer
mmap
Data processing task
Read and process values from the Ring Buffer
Store result
Signal

---
Performance results
Data stream capture from the device under test
Data Rate: 115200 Baud
Interrupt Rate: 1.3 ms
Maximum Latency (Interrupt -> Readout last byte): 380us
Ringbuffer size: 256kiB
Max. Filllevel: 160 kiB

---
Is Preempt-RT production ready ?
It depends.
The development process has stabilized
Productized versions are necessary (not every single -rt release is usable)
Used already in products:
  - Laser control
  - Wood working machines (multi axis servo control)
  - Soft-PLC (ARM, PPC based)